## Slide 1
Distributed Acoustic Sensing (DAS) for marine geosciences
Geoazur DAS team: Anthony Sladen, Diane Rivet, Jean-Paul Ampuero, Diego Mercerat, Daniel Mata, Gauthier Guerin, Itzhak Lior

## Slide 2
Laser source
~10 ns
Sensing unit
2-7U
Fibre optic cable (~50 km)
Reflected light signal
(Rayleigh scattering)
100-600 Watts
Advantages:
Long range >100 km
Distributed = one sensor every meter
Simple maintenance: interrogator at one end
Low cost: few $ / meter fiber + 100 k$ interrogator
Principle and advantages of DAS

## Slide 3
“Distributed Acoustic Sensing Turns Fiber‐Optic Cables into Sensitive Seismic Antennas”
(Zhan, SRL 2020 review paper)
Seafloor DAS Geo Geoazur - Sladen et al (2019) Caltech - Williams et al (2019) Berkeley – Lindsey et al (2019)
DAS recording of a M4.5 earthquake 150 km away
1 m spacing between channels

## Slide 4
Two complementary strategies
Installing dedicated cables
Using existing seafloor telecom cables

## Slide 5: DAS Geoazur team publications
A. Sladen, D. Rivet, J. P. Ampuero, L. De Barros, Y. Hello, G. Calbris, P. Lamare, Distributed sensing of earthquakes and ocean-solid Earth interactions on seafloor telecom cables, Nature Comms., 2019
I. Lior, A. Sladen, D. Rivet, J. P. Ampuero, Y. M. Hello, P. Lamare, C. Jestin, S. Tsagkli, C. Markou, On the detection capabilities of underwater DAS, J. Geophys. Res., 2020
I. Lior, A. Sladen, D. Mercerat, J.-P. Ampuero, D. Rivet and S. Sambolian, Strain to ground motion conversion of DAS data for earthquake magnitude and stress drop determination, Solid Earth, 2021
Rivet, D., de Cacqueray, B., Sladen, A., Roques, A., Calbris, G., Preliminary assessment of ship detection and trajectory evaluation using Distributed Acoustic Sensing on an optical fiber telecom cable, JASA, 2021
M. van den Ende and J. P. Ampuero, Evaluating seismic beamforming capabilities of Distributed Acoustic Sensing arrays, Solid Earth, 2021
M. van den Ende, I. Lior, J. P. Ampuero, A. Sladen, A. Ferrari, C. Richard, A self-supervised Deep Learning approach for blind denoising and waveform coherence enhancement in Distributed Acoustic Sensing data, EarthArXiv preprint, 2021
I. Lior, D. E. Mercerat, D. Rivet, A. Sladen, J. P. Ampuero, Imaging an underwater basin and its resonance modes using optical fiber Distributed Acoustic Sensing, EarthArXiv preprint, 2021

## Slide 6
Seafloor
fiber optic cable
DAS interrogator
Distributed sensing of earthquakes on seafloor telecom cables
Sladen et al. (2019)

## Slide 7
Seafloor
fiber optic
cable
Seafloor
fiber optic cable
Seismic station
Seismic
station
Recordings of a M1.9 micro-earthquake 100 km away
Distributed sensing of earthquakes on seafloor telecom cables
Sladen et al. (2019)

## Slide 8
Seafloor recordings of a M3.4 earthquake in Greece
Comparison with ocean bottom seismometer. S and surface waves are visible

## Slide 9
Detection Capabilities of Underwater DAS Lior et al (2020)
Ground acceleration (power dB)
km s
Seismometers
DAS

## Slide 10
①
②
Location Capabilities of Underwater DAS Martijn van den Ende (Geoazur)
Apparent speed
= (true speed)/sin(i)
Radial axis = slowness = 1/speed

## Slide 11
Imaging an underwater basin and its resonance modes Methoni Bay, Greece
Lior et al (2021)

## Slide 12
Ocean gravity waves
ω = √g.k.tanh(k.h)
Sladen et al (2019)

## Slide 13
x
time
Vibration of suspended cable portions Daniel Mata

## Slide 14
Five-minute averages of strain rate power
Toulon cable
Temperature fronts? Deep sea currents?
Long-period deep sea dynamics
Notes: Toulon cable

## Slide 15: DAS-Ligure
Câble telecom décommissionné de Monaco à Savone. 140 km + DAS = 14 000 capteurs sismo-acoustiques
Ligurian fault system Star = 1887 earthquake epicenter
(Larroque et al, 2012)
Notes: https://doi.org/10.1111/j.1365-246X.2012.05498.x

## Slide 16: INITIATIVE FOR DISTRIBUTED FIBER OPTIC OCEAN OBSERVATORIES ​(ID-FOO)
AAP “Un océan de solutions”
Fédère communauté nationale sur l’exploitation des données DAS pour étude de l’océan
15 labos, 50 chercheurs,
Projet 2.5M€ sur 5 ans
Centré sur cable Ligure et autres (Toulon, Mayotte, experiences...)
Thèmes abordés :
  Paysage sonore
  Mammifères marins
  Hydrodynamique côtière
  Circulation océanique via microsismique et température
  Tomographie de la colonne d’eau

## Slide 17
Sample of DAS data on the Ligure cable
Secondary microseism

## Slide 18
22 times:
150 km long DAS arrays
37500 sensors each
4 m spacing between sensors
DAS-Chili Diane Rivet ERC ABYSS proposal
Notes: La technologia DAS transforma une cable de fibra optica en milles des sensores distribuido a lo largo del cable hasta distancia de 150km. Se connecta a una extremidad del cable, sole necesita un instrumento el interrogador, qui contiene une laser y un interferometro. Durante su trayecto a travers la fibra, parte de la luz se develve asia el instrumento, se llama back scattered light, luz retro difusada.

## Slide 19
Probe the mechanical state of a fault prior to large earthquakes using seismic waves.
Transform the way we make
real-time early warning
for offshore earthquakes.
Dense Permanent
Remote Real-time
Expected breakthroughs:
DAS-Chili Diane Rivet ERC ABYSS proposal

## Slide 20
50 secondes
Pilot experiment Oct-Nov 2021
Mw 4.8 08/11/2021 06:16:30
130km

## Slide 21
New Caledonia - Vanuatu SMART cable initiative
Future cable Lifou to Port Vila, ~300 km
IRD funding to add DAS
Moore Foundation funding to develop geophysics applications

## Slide 22
DAS-Peru – J.P. Ampuero ERC proposal

## Slide 23: Marine DAS : a key moment for the French seismology community
France has pioneered marine DAS, but more teams are now investing on it (USA, Japan, Spain, Portugal)  need to keep moving forward
So far, experiments have been short-duration  need for long-term observation
So far, data access has been restricted  need open data to accelerate broader use
So far, experiments have been led and analyzed by seismologists  need to train other communities for multi-disciplinary use