## Slide 1: MachineLearning and Distributed Acoustic Sensing: A case study
18 November 2021

## Slide 2
General principle of Distributed FO Sensing

## Slide 3: General principle of fiber optic distributed sensing
DTS: Distributed Temperature Sensing
DSS: Distributed Strain Sensing
DAS: Distributed Acoustic Sensing
DTS DSS DAS
A pulse of light is sent through the fiber
Back-scattering effect occurs continuously everywhere along the fiber
The backscattering light contains information from where it was generated
Operation is repeated to increase S/N (DTS, DTSS) or access the dynamic (DAS)

## Slide 4: From optic to acoustic
-> Need direct access to the phase of the pulse
-> Need to differentiate the phase of the light through the gauge length
Without differenciation
With differenciation
df-OTDR - Phase-based DAS and Gauge length
Pulse propagating
Information of longitudinal strain applied on the optical fiber is contained on the phase of the optical pulse travelling to it
Scattering has a fixed phase relation to the incident light

## Slide 5: df-OTDR - Phase-based DAS
Fiber distance
Optical power
Pulse width
Pulse rate frequency
Spatial sampling resolution
Gauge length
Derivation time (if strain-rate)
Parameters to adjust :
Acquisition parameters
A.H. Hartog, An Introduction to Distributed Optical Fibre Sensors, CRC Press, 2017

## Slide 6
Context

## Slide 7: Pipeline Monitoring
Risk identification:
Leaks,
Natural hazards,
Anthropogenic hazards,
Intrusion

## Slide 8: Pipeline Monitoring
Challenges:
Use of DAS for risk identification.
Handle the large amounts of data generated by DAS acquisitions.
Release an accurate alert if necessary.
Solution:
Use of Machine Learning techniques for event classification.

## Slide 9
The algorithm

## Slide 10: The Random Forest algorithm
A supervised Machine Learning algorithm developed by Breiman in 2001
Proved its interest in seismology for classification of environmental sources, tectonic events or nuclear explosions
Use of a large number of decision trees constituing a forest.
Training set:
Class determination
Discriminating attributes:
Duration
skewness
fmax
Kurtosis
Spectral properties
50+ features
Random Forest algorithm
…
Tree 1
Tree 2
Tree n
Decision = Classification
1
1
2
4
5
6
3
7

## Slide 11: The Processing chain
Signal event
Database
Machine Learning
with Random
Forest algorithm
Signals
Classification
Alert release if
Identified danger
Signal event
Database
(Sub-Samples)
Training chain
Class 1
Class 2
…
Database
1
2
4
5
6
3
7

## Slide 12: Implementation of the algorithm for real time monitoring
For now, the used approach was a succession of signal detection and classification.
Our approach is based on an analysis and classification in flow with a fixed time window.
Addition of a new class: the ambient noise.
LTA
STA
STA/LTA detection approach
Flow approach

## Slide 13
The event catalogues

## Slide 14: The event catalogues
Located in Pau, South-West of France.
State-of-the-art test center to simulate site conditions.
Designed to qualify Distributed Fibre Sensing in various conditions.
Numerous applications can be tested:
  Pipeline leak detection of both gas and liquid with pressure up to 50 bars: 3 different sizes, positions and orientations of leaks
  Third party intrusion
  Ground movement/landslides
  PIDS
  Cable/umbilical monitoring
  And more on demand
FEBUS Optics’s test Center

## Slide 15: The event catalogues
Various fibre-optic cables: Single-Mode, Multi-Mode fibres in tight or loose tube, directly buried in the ground or inside conduits and at various distances from a buried pipe.
Different events: falling objects, compactor, foot steps, vehicles.
Events recorded with FEBUS A1-R DAS system.
Class | Number of windows
Ambient noise | 388625
Falling objects | 55425
Compactor | 179600
Vehicle | 117680
Pedestrian | 73325

## Slide 16
Results of classification

## Slide 17: Results of classification
Class | Number of windows
Ambient noise | 388625
Falling objects | 55425
Compactor | 179600
Vehicle | 117680
Pedestrian | 73325

## Slide 18: Results of classification
Real time classification

## Slide 19
Conclusions

## Slide 20: Conclusions
We demonstrated in this work the ability of the Random Forests algorithm, a supervised Machine Learning algorithm, for the classification of event recorded with DAS system.
The training dataset, well labelled and equilibrated, appears of a large importance to obtain the best quality of event identification.
Other tests are planned to be conducted in order to grow the training dataset with a large variety of sources such as leaks or landslides. This will enable to experience, test the limits, and improve the efficiency of our classification algorithm.

## Slide 22: Scattering mechanisms
glass scattering structures
Rayleigh scattering
Raman scattering
Brillouin scattering
Static glass inhomogeneities
Intra-molecular bond vibrations
vib in the THz frequency range
amplitude of vibrations depends on T
Inter-molecular vibrations
Propagating wave
vib in the GHz frequency range
frequency depends on temperature and strain
‘Frozen’
waves
Waves
moving
with wind
Individual
Grains of sand
moving
with wind

## Slide 23: Scattering mechanisms
 | Temperature | Strain (static or slow) | Acoustic | Optical measurement
Raman |  |  |  | Intensity ratio
Brillouin |  |  |  | Frequency shift
Rayleigh |  |  |  | Phase shift
Summary table
( )
( )